POOL FINAL INSPECTION

# Application#_________Date:_____________

# Location:______________________________

(A) – All items approved      (C) – Correction needed/work incomplete      (N/A) – Not applicable

INTERNATIONAL SWIMMING POOL & SPA CODE 2018 EDITION

| Code Section | Item or Description | (A), (C), (N/A) |
| --- | --- | --- |
| ASTM F1346 | Pool/Spa Covers as Barriers |  |
| 305.2.2 | Barrier Openings |  |
| 305.2.4 | Barrier Climb ability |  |
| 305.2.1 | Barrier Height and Clearances |  |
| 305.3 | Access Gates/Latches |  |
| 305.4 504.1.1 | Alarms/KATIE BETH'S LAW POOL ALARM TCA 68-14-802 |  |
| 322 | Ladders/Recessed Treads |  |

(   APPROVED

| Code Section | Item or Description | (A), (C), (N/A) |
| --- | --- | --- |
| 811 | Rope w/Floats required at Point of First Slope to Deep End of ALL Inground Pools |  |
| 314 | Suction Fitting outlets shall be designed and installed in accordance with ANSI/APSP-7 |  |
| 310 | Suction Entrapment Avoidance(dual drains, grate size, etc.) |  |
| 313.7 | Emergency Shut Off Provided on Commercial Applications Must Be Visible & within 5’Horizontally of Inside Pool/Spa Walls |  |
| 321 | Lighting Provided for Commercial Pools Open During Low Light Hours |  |
| MoCo | Electrical Inspections Completed/Approved |  |

(   DISAPPROVED

| CODE SECTION | COMMENTS, CORRECTION NEEDED, OR WORK INCOMPLETE |
| --- | --- |

PASSED		FAILED, REINSPECTION REQUIRED		$50 FEE REQUIRED

Inspector’s Signature:

## POOL REQUIREMENTS

All outdoor pools, spas and hot tubs with water over 24" deep, must be protected with a barrier as outlined below.

Height:		48" minimum above grade measured from the outside face of the barrier.

Openings: 	2" maximum between grade and bottom of barrier

- 4" maximum between top of above-ground pool wall and bottom of barrier when barrier is attached to top of pool wall.

- All other openings shall not allow the passage of a 4" diameter sphere.

Climbability: 	Solid barriers (stone walls, etc.) must have no protrusions or indentations.

- Horizontal members less than 45" apart must be located on the inside face of the barrier. In such cases, the space between corresponding vertical members must be 1.75" or less.

- Maximum mesh size for chain link fences shall be a 2.25-inch square unless the fence is provided with slats fastened at the top or the bottom which reduce the openings to not more than 1.75 inches.

- Decorative cut-outs within a vertical member must not have openings greater than 1.75".

Access Gates:

- Must meet height, opening and climbability requirements for barriers.

- Must be self-closing and self-latching, and must open outward away from pool.

- Latches less than 54" from the bottom of the gate must be located on pool side at least 3" from top of the gate. There shall be no openings 1/2" or greater within 18" of the latch.

- Latches located greater than 54" from the bottom of the gate may be located on both sides.

Doors alarms: (equipped on doors which open from house directly to pool area)

- Must sound immediately and continuously for 30 seconds.

- Must be heard throughout the house.

- Must reset automatically.

- Must be able to be temporarily, but not permanently deactivated. mechanism to deactivate must be 54" above the door threshold.

Pool Alarm:

- Must be installed in pool and operational before final pool inspection

Spas and Hot Tubs:

- Safety covers may be substituted for barriers provided such covers meet     standard ASTM F1346.

- Mechanism to deactivate must be 54" above the door threshold.

Entrapment protection:

- Suction Outlets shall be designed to produce circulation throughout the pool or spa shall be protected against user entrapment.

- Shall be protected by a 12” X 12” drain grate or larger or equivalent that meets ANSI/ASME A112.19.8M or an approved channel drain system.

- Atmospheric vacuum relief system required. Should grate covers become missing or broken. The vacuum relief system shall include at least one approved or engineered method:

  - Safety vacuum release system conforming to asme a112.19.17 ,or an  Approved gravity drainage system.

- Dual Drain Separation:

  - Minimum of 2 suction outlets of the approved type.

  - Minimum distance of 3 ft horizonal or vertical separation between suction outlets.

  - They shall be piped so that water is drawn through them simultaneously through a vacuum relief-protected line to the pump or pumps.

- Pool Cleaner fittings shall be located in an accessible position(s) at least 6 inches and not greater than 12 inches below opeational water level or as an attachment to the skimmers

# Text boxes

MONTGOMERY COUNTY GOVERNMENT

BUILDING AND CODES DEPARTMENT

350 Pageant Lane, Suite 309

Clarksville, TN 37040

Phone 931-648-5718 Fax 931-553-5121

www.mcgtn.org